## Slide 1: Electronic Systems Design Methodology
Santosh S Malagi - v01

## Slide 2
Electronic Systems Design Methodology © 2024 by Santosh S Malagi is licensed under CC BY-SA 4.0. To view a copy of this license, visit http://creativecommons.org/licenses/by-sa/4.0/

## Slide 3
Contents
Motivation
Electronic Systems – an Overview
Electronic Systems Design
  Standard Cell-Based ASIC Design
  FPGA based Design
  Analog VLSI Design
  Mixed-Signal VLSI Design
Executing Design Methodologies using EDA tools
Summary
References and More Resources

## Slide 4: motivation
Who? What? and Why?

## Slide 5: What?
Economics of Electronic Systems Design (ESD)
  Understand various market players - EDA/IP, fabless, fablite, foundry etc.
Introduction to basics of Electronics Systems Design Methodology
  VLSI design methodologies – Digital, Analog and Mixed-Signal
  Various EDA tools involved in the design process
  ‘Hardware-Software Co-design’ using ‘Platform SoCs’ or ‘MpSoC’s’
What is NOT covered?
Transistors, semiconductor physics etc. deliberately left out to focus on higher levels of abstraction
Memory design will be included in future revisions
Analog design (the presenter is a ‘Software Engineer’ who writes C++ but knows a bit of DFT/ATPG) 
Advanced topics in Physical Design and Implementation – beyond author’s level of expertise

## Slide 6: Why?
‘Software Engineers’ interested to learn more about VLSI and chip design flow
Many want to learn about different EDA tools and how they fit in the overall design flow
Stuff you don’t learn in EE/ECE/CE curriculum but are expected to pick up on your own
Clarify basic terminology and three-four letter acronyms - VLSI, ASIC, ASSP, SoC etc.
Provide pointers and useful references for those looking for more
Collection of ‘Personal Notes’ and ‘Illustrations’ attempts to cover the following topics:
Electronic Systems Design Methodology
EDA Software
VLSI Test Engineering
The depth of material is akin to a ‘motivational’ or ‘101’ lecture given in relevant EE/CE courses
Limited to my knowledge and experience gained in the past 4.5 years

## Slide 7: Electronics Systems – an overview
Integrated Circuits (IC), economic impact and the design ecosystem

## Slide 8: Preliminaries
Integrated Circuit (IC) – electronic circuit fabricated on a single piece of semiconductor material
Wafer – extremely thin circular disk of semiconductor material used to fabricate multiple ICs
Die – individual IC ‘sliced’ from a wafer, ‘naked die’ before packaging
Chip (aka microchip) – an IC which is hermitically sealed/packaged
Printed Circuit Board (PCB) – polysilicon material used to interconnect and hold together several chips to form an ‘Electronic System’

## Slide 9: Electronic Systems Evolution
Clock
ASIC
DAC
ADC
ROM
Chip 1
Chip 2
DSP
µP
RAM
ASIC
Printed Circuit Board with multiple ICs
µP
µP
RF Modem
Core
DAC
ADC
Memory
Memory
GPU
PLL
Function Specific Logic
Bus architecture
DSP
Interface
System on Chip (SoC)
Software
Platform SoC

## Slide 10: Global Electronic Systems Market – by Numbers
Electronics is a major contributor to the world GDP, enabler of the modern ‘digital economy’
Annual growth rate of 6.67%, sales increased from $139.0 billion in 2001 to $574.0 billion in 2022
Significant R&D investment, requires skilled labor and value creation through ‘product differentiation’
Reference – Semiconductor Industry Association (SIA) Factbook 2023
Global Electronics Sales in billion USD

## Slide 11: End Markets for Electronic Systems
Chart: 2021 Semiconductor Consumption
| Computing | Communications | Automotive | Consumer | Industrial | Government
Consumption | 175.6 | 170.6 | 69.1 | 68.4 | 66.9 | 5.8
Reference – 2022 State of the US Semiconductor Industry Report - SIA
Electronic Systems – Application Areas:
Computing
  Cloud and distributed systems, PC, office equipment, tablet PCs etc.
Communications
  Wired/Wireless devices, routers, switches, networking, telecommunication infrastructure etc.
Automotive
  ECU, infotainment, power train, safety, ADAS etc.
Consumer
  All kinds of consumer appliances – smart TVs, digital cameras, smartphones, medical devices etc.
Industrial
  Industrial automation and robotics, manufacturing, monitoring, surveillance, etc.
Government
  Defense, aerospace etc.

## Slide 12: Who are the Market Players?
Electronic Design Automation/IP Vendors - software tools, virtual components, IP blocks etc.
Fabless companies - design chips, outsource manufacturing/packaging/test to foundry/OSATs
Integrated Device Manufacturer (IDM) – design and fabricate chips in house
Fablite companies - outsource standard wafer processing, retain specialized manufacturing
Foundry - wafer processing, chip fabrication, heterogenous integration etc.
Equipment – design and manufacture technology for chip fabrication, packaging, test etc.
Outsourced Semiconductor Assembly and Test (OSAT) and Contract Manufacturers
Materials Providers – semiconductor materials, chemicals for chip fabrication, packaging etc.
More….

## Slide 13: Integrated Circuits – Digital, Analog, and Mixed-Signal
Digital ICs - operate on discrete logic high ‘1’ or logic low ‘0’ signal levels
Analog ICs – operate on continuous time varying signals between two levels
Mixed Signal ICs – operate on both digital and analog signals, often convert between the two (DAC, ADC)
Digital
Logic
  General purpose
  Microprocessor (CPU)
  Graphics Processing Unit (GPU)
  Microcontroller (MCU)
  Field Programmable Logic (FPL)
  Memory
    Volatile – SRAM and DRAM
    Non-volatile – ROM, Flash etc.
Mixed-Signal
Analog to Digital Converters (ADC)
Digital to Analog Converters (DAC)
Digital Signal Processors (DSP)
Delta-Sigma Modulators
Error Detection/Correction ICs
Analog
Single-stage Amplifiers
Differential Amplifiers
Operational Amplifiers (OpAmps)
Power Amplifiers
Comparators
Radio Frequency Integrated Circuits (RFIC)
Phase Locked Loops (PLLs)
Others
Micro-Electro Mechanical Systems (MEMS)
  Sensors
  Actuators
Photonic/Optoelectronic ICs
Emerging Technologies

## Slide 14: Integrated Circuits – Market’s Perspective
General Purpose IC
  Generic functionality, IC sold in huge quantities e.g., 74xx, 555, RAM, ROM etc.
Application Specific Integrated Circuit (ASIC)
  IC designed for a specific purpose/application area
  Application Specific Standard Product (ASSP)
    IC designed and optimized for a specific purpose, sold to numerous customers
    E.g., Qualcomm sells Snapdragon processors to Samsung, MediaTek, Lenovo etc.
  User Specific Integrated Circuit (USIC)
    IC designed and optimized by a company for its specific use case, product differentiation
    E.g., Apple designs ‘Apple Silicon’ for use ONLY in Apple products
What is a System on Chip (SoC)?
A SoC is an ASIC which integrates a complete computing system on a single chip (SiP – System on Package). Most often an SoC includes a Central Processing Unit (CPU), Graphics Processing Unit (GPU), embedded memory (SRAM), RF modem, sensors, I/O interfaces along side specialized hardware e.g., hardware accelerators on a single substrate or microchip.
*All SoCs are ASICs, but all ASICs need not be SoC’s!

## Slide 15: System on Chip (SoC)
µP
µP
RF Modem
Core
DAC
ADC
Memory
Memory
GPU
PLL
Function Specific Logic
Bus architecture
DSP
Interface
System on Chip (SoC)
Software
Platform SoC
A SoC combines multiple stand-alone circuits on a single silicon substrate – thereby creating a complete ‘System on Chip’
‘Platform SoC’ = ‘Software Stack’ + SoC
MpSoC = Multiprocessor System on Chip, SoC with multiple processors
Benefits to the SoC approach:
  accommodate “increased functionality for the same price”
  reduce the number of discrete components – hence the points of failure
  faster, powerful systems at reduced price
What enabled the SoC revolution?
  Continued progress in IC fabrication technology
  EDA tools, IP ecosystem and design methodologies
  Market drivers – demand for more functionality
Smaller
Faster
Cheaper
Reliable
Powerful

## Slide 16: Microprocessors (µP), Microcontrollers (µC), vs System on Chip (SoC)
CPU
ALU
Registers
µP
RAM
ROM
Counters
Timers
GPIO
µP
µP
µP
µP
GPIO
RAM
ROM
Timers
Counters
GPU
RF
DAC
ADC
CODECS
More…
DAC
ADC
Microprocessor:
General purpose computing
I/O devices and memory are interfaced externally
Microcontroller:
Embedded computing
µP + memory + I/O devices + other basic peripherals
usually, single µP core
System on Chip (SoC):
Complex applications
multiple µP + memory + I/O devices + RF + GPU + ….
Sophisticated computing system on a chip

## Slide 17: EDA/VLSI in the OSI Model
Content
Network
Hardware
Compilers
Applications
Services
Systems Programming
End User
Electronic Design Automation
Chip-design
Hardware-Software Co-design/verification

## Slide 18: Electronic Systems DESIGN
How to design Electronic Systems?

## Slide 19: Electronic System Design – Traditional Design Methodology
User inputs
Requirements and Specification
Architecture Design Space Exploration (DSE)
Hardware Architecture (Analog/Digital Partitioning)
Analog VLSI Design
Digital VLSI Design
Mixed-mode System Verification
Software Architecture
Software Design
Software Testing
Design loop
Post-Silicon Validation and Debug
Maintenance/Field Debug
Drawbacks of Traditional Electronic System Design Flow:
Hardware architecture is designed and implemented first
Software development can only start after prototype hardware is available
Longer TTM – hardware-software design loop

## Slide 20: Electronic Systems Design – Hardware/Software Co-design Methodology
Software Architecture
User inputs
Software Design
Software Testing
Post-Silicon Validation and Debug
Deployment
Hardware Architecture (Analog/Digital Partitioning)
Analog VLSI Design
Digital VLSI Design
IC Fabrication and Packaging
Software Build/Application
Hardware-Software Co-verification
Rapid Prototyping
Hardware Software Integration and Simulation/Emulation
Mixed-mode System Verification
Requirements and Specification
Maintenance/Field Debug
Architecture Design Space Exploration (DSE)
Hardware/Software Partitioning

## Slide 21
Front End Design
Define Overall Architecture
Behavioral Modelling
Block-level Functional Specification
Block-level RTL design
Verification
ATPG
Logical Equivalence Check (LEC)
Partitioning Floorplanning Power and Ground Routing Placement Clock Tree Synthesis Global Routing Detailed Routing Sign-off STA
Block-level RTL Simulation
RTL power/timing verification
Gate Level Simulation (GLS)
Formal Verification
Emulation
Physical Design
Design Rule Check (DRC) Layout vs Schematic (LVS)
Antenna Effects Electrical Rule Check (ERC) Parasitic Extraction Signal and Power Integrity
Physical Verification
Sub-block Integration
Layout Post Processing, ECO
Mask Generation
Fabrication
Logic Synthesis
Test Structure Insertion (DFT)
System Level Specifications
Back End Design
Standard Cell-Based ASIC Design
IP
Standard-cell Library
PDK
GDSII
Test Vectors
RTL to GDSII flow = Front End + Back End Design Flow
PDK – Process Design Kit

## Slide 22: FPGA based Design
Field Programmable Gate Array (FPGA)
  pre-defined ‘Look Up Tables’ (LUTs), hardware resources which can be programmed using a ‘bit stream’
FPGAs vs ASICs
  Design Methodology
    ASIC design methodology = RTL to GDSII flow (Front End + Back End Design)
    FPGA design methodology = digital design → generate bit-stream → program FPGA device → deploy
  ‘Reprogrammable’
    ASIC is ‘cast’ in Silicon → cannot be modified unless there is a ‘respin’ or new design, system level changes only possible through software programming if ASIC embeds a CPU/GPU/DSP etc.
    FPGA is ‘Field Programmable’ i.e., a new digital design can be remapped to hardware and redeployed on the fly. Modern FPGAs embedded with a CPU are called ‘Embedded FPGA Processors’ or ‘SoC FPGAs’ or ‘FPGA SoCs’
  Others
    FPGA based systems often have high production cost (this is changing overtime), mostly suited for low volume
    ASIC performance is generally better than FPGAs
    FPGAs are a very good prototyping vehicle or for products requiring constant ‘reconfigurability’.
Design Entry or HDL Design
Functional (RTL) Simulation
Logic Synthesis
Device Mapping Place and Route
Static Timing Analysis (STA)
Bitstream Generation
Requirements
Design suite provided by FPGA/EDA vendor
FPGA programming

## Slide 23: Analog VLSI Design
PDK – Process Design Kit
Device Library
Technology Data
Rule Files Simulation Models
Analog IP
PDK
Circuit Specifications
Architecture Design and Partition into Blocks
Circuit Design
Circuit Simulation
Circuit Calibration
Custom Layout Design
Layout Verification
Parasitic Extraction
GDSII for Fabrication
Analog IC Design:
Analog circuits interface and manipulate continuous time arbitrary electrical signals
Analog circuit design is considered a ‘Black Art’
Analog design automation still today mostly remains an ‘elusive research topic’
Analog circuits WILL always remain relevant and can play a significant role in the AI chip revolution
“Analog Circuit designers are scarce, VERY WELL
compensated, gain lots of respect, and often regarded as Artists” - a well known adage in the VLSI industry!

## Slide 24
Mixed-Signal Design
System Specification
Hardware Architecture (Analog/Digital Partitioning)
IP
Standard-cell Library
PDK
Device Library
Technology Data
Rule Files Simulation Models
Analog IP
PDK
Architecture Design and Partition into Blocks
Circuit Design
Circuit Simulation
Custom Layout Design
Layout Verification
Block-level RTL design
Verification
Physical Design
Physical Verification
Logic Synthesis
DFT and ATPG
Top-level mixed mode simulation
Floorplanning
Top-level Routing
DRC and LVS
Post Layout Simulation
Layout Post Processing
Mask Generation
Analog VLSI Design Flow
Digital VLSI Design Flow

## Slide 25: Executing Design Methodologies using EDA tools
EDA Methodology in Practice
© Santosh S Malagi 2023

## Slide 26: Design Methodologies – ‘Top-Down Approach’
Daniel-Gajski Y Chart
Reference – Top-Down VLSI Design, Figure 1.10
Front-end design
Back-end design
module dff (CK,Q,D);
input CK,D;
output Q;
reg Q;
always @ (posedge CK)
Q <= D;
endmodule
module And_DFF_Or(in1,in2,in3,CK,out1);
input in1,in2,in3,CK;
output out1;
wire w1,w2;
and AND1(w1,in1,in2);
dff DFF1(CK,w2,w1);
or OR1(out1,w2,in3);
endmodule
module And_DFF_Or(in1, in2, in3, CK, out1, SCAN_EN, SCAN_IN, SCAN_OUT);
input in1, in2, in3, CK, SCAN_EN, SCAN_IN;
output out1, SCAN_OUT;
wire in1, in2, in3, CK, SCAN_EN, SCAN_IN;
wire out1, SCAN_OUT;
wire n_0;
OR2X1 g11__2398(.A (in3), .B (SCAN_OUT), .Y (out1));
SDFFQX1 DFF1_Q_reg(.CK (CK), .D (n_0), .SI (SCAN_IN), .SE (SCAN_EN),
.Q (SCAN_OUT));
AND2X1 g13__5107(.A (in1), .B (in2), .Y (n_0));
endmodule

## Slide 27: ‘Design Methodology’ and ‘Tool Flow’ Example
Block-level RTL design
Verification
ATPG
Logical Equivalence Check (LEC)
Physical Design
Physical Verification
Sub-block Integration
Layout Post Processing, ECO
Mask Generation
Logic Synthesis
Test Structure Insertion (DFT)
Overall Design Goals:
Achieve high (99%) stuck-at and 85% transition fault coverage.
Test Methodology:
DC pin test parametric test
Test logic verification
DC logic stuck-at
At-speed logic delay
Memory testing
Iddq testing
Specialty testing
  Analog
Burn-in testing
Setup tool environment
Read design netlist
Read standard-cell Verilog
Build ATPG design model
Setup constraints
Build chip testmodes
DRC checks
Enumerate list of faults
Generate scan-chain tests
Generate stuck-at ATPG patterns, simulate to calculate FC
Generate two-cycle transition ATPG patterns, simulate to calculate FC
Compact and write out Vector set in required format
ATPG Tool Flow
‘Tool Flow’ helps execute a ‘Test Methodology’ to achieve the overall ‘Design Goal’.
DFT methodology influences the ATPG methodology or the other way round. It also impacts the Physical Design flow.

## Slide 28: Summary

## Slide 29: Future Developments in ‘Design Methodologies’
Design methodologies will continue to address the following challenges:
Hardware-software co-design and verification
  SoC’s increasingly involve multiple IPs (often from multiple vendors) connected by a bus architecture
  Verification complexity increases proportionately with design complexity
Design for Testability
  dealing with newer defect mechanisms in advanced nodes, low pin count testing and cost of testing
Design Integrity
  cross talk, IR drop, timing closure, Electromigration (EM), Electrostatic Discharge (ESD)
3DIC Integration and Packaging
  Integrating heterogenous cores (digital, analog, memory etc.) and 3D IC integration
Power, Thermal and Timing
  Timing closure – ensuring design meets the timing checks and requirements
  Higher power = hotter chips!

## Slide 30: Summary
Electronic systems form the backbone of the modern digital economy
Multiple players – EDA/IP, fabless, foundry, IDM’s etc. make up the semiconductor value chain and ecosystem
A System on Chip (SoC) - integrates a complete computing system on a single chip
Today’s electronic systems are mostly developed using ‘Hardware-Software Co-design Methodology’
Design methodology - sequence of steps needed to convert a ‘concept’ into ‘working silicon’
Successful design methodology development is a multi-disciplinary endeavor
  Hardware architecture and systems engineering
  Circuit Design (digital and analog)
  Verification technologies
  Test Engineering
  Fabrication, physical layout design and semiconductor physics
  Expertise in use of advanced EDA tools, tool scripting etc.
  Optimum use of compute resources
  Design Data Management
“There is no single right way to design a chip, but sure there are many wrong ways.”
-Anonymous

## Slide 31: References
Kaeslin, Hubert. Top-down digital VLSI design: from architectures to gate-level circuits and FPGAs. Morgan Kaufmann, 2014.
Dillinger, Thomas. VLSI Design Methodology Development. Prentice Hall, 2019.